## Slide 1: Dual Decomposition of ACOPF
Anirudh Subramanyam
Youngdae Kim
Mihai Anitescu
May 26, 2020

## Slide 2: Goal: Multiperiod security-constrained ACOPF
Idea
Decompose into single-period single-scenario problems
Coordinate their solution towards overall optimum using dual multipliers
Advantages
Scalable with respect to number of time periods/scenarios
Can address problem sizes that would otherwise not fit in memory
Single-period/scenario problem is solver-agnostic (can be on CPU/GPU)

## Slide 3: Algorithm: Proximal Augmented Lagrangian
Can be shown to converge to a stationary point under certain assumptions
Practical convergence depends on formulation design and , ,
Initialize , , . For do
Compute using Jacobi update:
Update
Power balances, flow limits etc. in each period/scenario
Ramping constraints AGC/frequency control constraints
Notes: \begin{align*}
\mathop{\text{minimize}}\;\; & \sum_{t \in T} c_t(x_t) \\
\text{subject to} \; & x_t \in X_t \; \text{ for all } t \in T \\
& \sum_{t \in T} A_t x_t = b
\end{align*}
\begin{align*}
\mathop{\text{minimize}}_{x_t \in X_t}\;\; \Bigg\{ c_t(x_t) + (\lambda^{k})^\top \Big[A_t x_t + \sum_{s \neq t} A_t x_s^{k} - b\Big] \\
+\frac{\rho}{2}\Big\lVert A_t x_t + \sum_{s \neq t} A_t x_s^{k} - b\Big\rVert^2 + \frac{\tau}{2} \big\lVert x_t - x_t^{k} \big\rVert^2 \Bigg\}
\end{align*}
\begin{align*}
\lambda^k = \lambda^{k-1} + \rho \Big[ \sum_{t \in T} A_t x_t - b \Big]
\end{align*}

## Slide 4: Current Implementation1: Julia + Ipopt on CPU
Single-period/scenario optimization problems
Currently solved using Ipopt and distributed across several cores
Can be easily interfaced to use HiOP through Julia
Can also be integrated into DSP which is a generic dual decomposition package written in C++ by Kibaek Kim (ECP/ANL)
Dual updates and error computations
Can be easily ported to GPU within Julia itself
1https://github.com/exanauts/proxALM

## Slide 5: Preliminary results: Multiperiod ACOPF
T = 50 time periods
Ramping constraints
Warm-started using solution computed at previous time period in rolling horizon
~6s per single-period problem Non-decomposed (Ipopt): ~6min
~60s per single-period problem Non-decomposed (Ipopt): ~4h
Notes: \begin{align*}
\lvert Pg_{t} - Pg_{t+1} \rvert \leq \Delta_g
\end{align*}

## Slide 6: Preliminary results: contingency constrained
Linking constraints
Warm-start as before
Lot of time is spent converging duals: can stop when primal feasible
Large proximal parameter necessary but slows down convergence
~0.2s per single-scenario problem Non-decomposed (Ipopt): ~15s
~6s per single-scenario problem Non-decomposed (Ipopt): ~15min

## Slide 7: Ongoing and future work
Implement efficiencies: Nesterov acceleration, active set updates, parameter tuning
Extend the contingency constrained model to consider frequency control
Implement cross-decomposition: decompose both in scenarios and time
Solve real case over multiple time periods and under contingencies